## Slide 1: Stability and Feasibility of Constrained Optimal Control
Pascal Grieder
Automatic Control Laboratory ETH Zürich

## Slide 2: Content
Introduction to Receding Horizon Control
New Contributions
  A) Infinite Time Constrained Optimal Control Synthesis (Grieder, Borrelli, Torrisi, Morari)
  B) Stability & Feasibility Analysis of RHC
  (Grieder, Parrilo, Morari)
Conclusion

## Slide 3: Feedback Control for Constrained Systems
System:
    Discrete Linear Dynamics:
    Constraints on the state
    Constraints on the input
Objectives:
    Find a feedback law u=f(x) which drives the state to the origin.
    Stability (feedback is stabilizing)
    Feasibility (feedback exists)
    Optimality
    Low Complexity

## Slide 4: Receding Horizon Control for Constrained Systems
Solve Finite Time Optimal Control Problem
  such that and
  and implement u(0).
Compute the solution
  On-Line (MPC) by solving a QP of finite size at each time step
  Off-Line (RHC) by using multi-parametric quadratic programming. Results in a piece-wise affine feedback law u(0)=f(x(0)) defined over polyhedra. (Bemporad, Morari, Dua, Pistikopoulos, 2002)

## Slide 5: Example System
Double Integrator:
Objective function:
Constraints:

## Slide 6: Receding Horizon Control
Horizon N=3 ) 21 Regions

## Slide 7: Receding Horizon Control
State x(0) in region #12
Optimal feedback law U3(x(0))=[u0, u1, u2]=F12x(0)+G12
Apply optimal input u(0)=u0
F12= [-0.6180 -1.3792
0.0000 -0.0000
-0.0000 0.0000]
G12T=[-0.8997 1.0000 1.0000]
x(0) in
Region #12

## Slide 8: Receding Horizon Control
x(1) in
Region #8
State x(1) in region #8
Optimal feedback law U3(x(1))=[u0, u1, u2]=F8x(1)+G8
Apply optimal input u(1)=u0
x(0) in
Region #12

## Slide 9: Receding Horizon Control
Open-loop trajectory for x(0) (red) and for x(1) (blue) are not identical

## Slide 10: Receding Horizon Control
By iteratively computing and applying only the first input, the Receding Horizon Control (RHC) trajectory is obtained.

## Slide 11: Receding Horizon Control
In general, closed-loop stability and feasibility are not guaranteed !
No feasible input
sequence over
3 steps exists

## Slide 12: How can we guarantee stability & feasibility ?
Compute feasible positive invariant set for the unconstrained controller around the origin
Fix 1: Make horizon N long enough to reach
Fix 2: Impose as a terminal set constraint
x(N)
x(0)
[0,…,N-1]
[N,…,1]

## Slide 13: Drawbacks of Fix 1 – How long is long enough?
Fix 1: Make horizon long enough to reach
Chmielewski and Manousiouthakis (1996):
  Conservative estimate of . ( for double integrator)
Scokaert and Rawlings (1998):
Increase N on-line until x(N)2 ! Expensive
Notes: Mention Receding horizon

## Slide 14: Drawbacks of Fix 2 – Feasibility & Optimality?
Fix 2: Impose as a terminal set constraint:
First introduced by Keerthi and Gilbert (1988)
Feasibility problem:
Optimality may be lost because of “forced” trajectory
x(0)
x(N)

## Slide 15: Content
Introduction to Receding Horizon Control
New Contributions
  A) Infinite Time Constrained Optimal Control Synthesis (Grieder, Borrelli, Torrisi, Morari)
  B) Stability & Feasibility Analysis of RHC
  (Grieder, Parrilo, Morari)
Conclusion

## Slide 16: New Contributions
Infinite Time Constrained Optimal Control Synthesis:
  Exact computation of
  Explicit infinite horizon controller
  Stability, feasibility and optimality is guaranteed
  Yields maximum positive invariant set O1

## Slide 17: New Contributions
B) Stability & Feasibility Analysis of RHC:
  Determines stability and feasibility properties of a given controller.
  Ascertains if the positive invariant set obtained for horizons is equal to O1
  Yields low complexity controllers

## Slide 18: Content
Introduction to Receding Horizon Control
New Contributions
  A) Infinite Time Constrained Optimal Control Synthesis (Grieder, Borrelli, Torrisi, Morari)
  B) Stability & Feasibility Analysis of RHC
  (Grieder, Parrilo, Morari)
Conclusion

## Slide 19: Infinite Time Constrained Optimal Control Synthesis
Algorithm iteratively applies reachability analysis and mp-QP
We will now analyze the algorithm based on the double-integrator example…

## Slide 20: Off-Line Computation of the CLQR Initialization
Compute positive invariant set where the LQR controller is feasible. (Kerrigan 2000)
Positive invariant set

## Slide 21: Off-Line Computation of the CLQR Step 1
Take a “small” step over a facet
Take a “small” step over a facet

## Slide 22: Off-Line Computation of the CLQR Step 2
Solve QP with horizon N=1 to obtain a 1-step optimal region
Region computed with horizon N=1
“small” step

## Slide 23: Off-Line Computation of the CLQR Step 3
Compute subset of this region which enters in N=1 steps
(reachability subset)
Different Trajectories
All points in the orange
region enter the red region
in one step

## Slide 24: Off-Line Computation of the CLQR Step 4
If all points which enter in N=1 steps have been found,
set N=N+1 and restart the procedure

## Slide 25: Region Exploration for the Double Integrator

## Slide 26: 1 – Horizon Algorithm
Initialization:
Compute positive invariant set  and set the horizon to N=1
Loop: While not converged do
  1. Move over a facet
  2. Solve QP and use KKT to compute the region
  3. Compute reachability subset
  4. If all facets were covered, increase the horizon N=N+1,
  else goto 1.

## Slide 27: 1 – Horizon Algorithm
Simulation Experience
  Faster than an mp-QP with fixed horizon (Baotic 2002)
  Faster than the computations of Scokaert and Rawlings (1998)
  Faster than estimates of Chmielewski and Manousiouthakis (1996)

## Slide 28: Run Time Example – Double Integrator
Comparison of off-line computation time
N1 is not known in general.
Method | Run-Time (2.5 GHz)
1 – Horizon Algorithm | 15.7 sec
mp-QP for N1 =13 (Tondel, Johansen, Bemporad 2001) | 18.5 sec (not optimized)
mp-QP for N1 =13 (Baotic 2002) | 16.8 sec
mp-QP for Nest =12000 | …still running…

## Slide 29: Run Time Example – Double Integrator
Comparison of on-line computation time
Based on 1000 random initial states
Method | QP (N=2k N0) (Scokaert and Rawlings 1998) | “Brute Force” Region Identification (65 regions after merging)
Average-Case | 29 msec | 0.84 msec
Worst-Case | 140 msec | 31 msec

## Slide 30: Properties of the Infinite-Time Solution
Produces the maximum positive invariant set O1
Stability, feasibility and optimality for Receding Horizon Control are guaranteed
Drawback: High Complexity

## Slide 31: Properties of the Infinite-Time Solution
Produces the maximum positive invariant set O1
Stability, feasibility and optimality for Receding Horizon Control are guaranteed
Drawback: High Complexity

## Slide 32: Content
Introduction to Receding Horizon Control
New Contributions
  Infinite Time Constrained Optimal Control
  Synthesis (Grieder, Borrelli, Torrisi, Morari)
  B) Stability & Feasibility Analysis of RHC
  (Grieder, Parrilo, Morari)
Conclusion

## Slide 33: Feedback Control for Constrained Systems
System:
    Discrete Linear Dynamics:
    Constraints on the state
    Constraints on the input
Objective:
    Find a feedback law u=f(x) which drives the state to the origin.
    Stability (feedback is stabilizing)
    Feasibility (feedback exists)
    Optimality
    Low Complexity OPEN ISSUE

## Slide 34: Novel Analysis Method
Input: PWA state space partition
Objective: show stability & feasibility of controller
Output: Feasible & Stable for all time?
! Yes / Can’t say

## Slide 35: Feasibility
Positive Invariance ) Feasibility
Feasibility ; Stability (unit cycle)
How is the invariant set computed ?
No feasible input
sequence over
3 steps exists

## Slide 36: Feasibility - Computation
Input: PWA partition with regions i=1,..,L
Choose a region i and compute the subsets which enter region j in one step…
i=1
j=3
j=2
j=4

## Slide 37: Feasibility - Computation
…for all target regions j.
No transition
from i=1 to j=4
j=2
j=3
j=4
i=1

## Slide 38: Feasibility - Computation
…for all starting regions i.
Note that the resulting union of regions is in general non-convex and might not even be connected.
1.1
2
3
4
1.2
not part of O1
not part of O1
not part of O1
not part of O1

## Slide 39: Feasibility - Computation
2
3
4
1.2
1
Redo until the partitions converge.
This algorithm always converges…
…but not necessarily in finite time

## Slide 40: Stability - Computation
Find stabilizing quadratic Lyapunov function V(x)=x’ PL x
Where , if the state x(t) is in region i
XF is the set of states for which a feasible feedback law exists

## Slide 41: Stability - Computation
Formulated as an LMI
Region i: { x2Rn | Hi x· Ki }
With x(t) in region i:
Johansson and Rantzer (1998)

## Slide 42: Analysis
If PL can be found, the system is exponentially stable
Extension to allow for PWQ Lyapunov functions: V(x)=x’Qix+x’Li+Ci
A PWQ Lyapunov function always exists for solutions computed with horizons N¸ N1 (might not satisfy LMI)
Analysis procedure applicable to ANY receding horizon controller, provided an explicit solution exists

## Slide 43: Example – Double Integrator
Horizon | New Algorithm | Terminal Set Constrained
N=1 | 72.8% | 13.5%
N=2 | 87.2% | 26.8%
N=3 | 93.4% | 46.2%
N=4 | 98.8% | 67.6%
N=5 | 100% | 73.8%
N=11 | 100% | 100%
Percentage of the maximum positive invariant set O1 covered

## Slide 44: Example – 2nd Order System
2nd order system with constraints ||u||· 1 and ||y||· 20
Percentage of O1 coverage
Horizon | New Algorithm | Terminal Set Constrained
N=1 | 100% | 1.5%
N=2 | 100% | 1.9%
N=3 | 100% | 2.3%
N=4 | 100% | 2.7%
N=5 | 100% | 3.1%
N=38 | 100% | 100%

## Slide 45: Content
Introduction to Receding Horizon Control
New Contributions
  Infinite Time Constrained Optimal Control
  Synthesis (Grieder, Borrelli, Torrisi, Morari)
  B) Stability & Feasibility Analysis of RHC
  (Grieder, Parrilo, Morari)
Conclusion

## Slide 46: Conclusion
The explicit infinite horizon controller has been presented
Stability, Feasibility and Optimality of Receding Horizon Control has been made less restrictive with the presented algorithms.
Result analysis is far easier with the explicit mp-QP solution, since results from PWA systems can be used.
Reports and Downloads on http://control.ethz.ch/~grieder